## Slide 1: Sensor data

## Slide 2: This Lecture
Sensordata.
Setup and configuration.
How can we use sensor data?
Concrete examples
Data quality.
Inaccuracies and sources of error

## Slide 3: Sensordata
What is sensor data ?
When did it start?
Data sources on the vessel

## Slide 4: What is sensor data ?
Data is found in various forms:
0-20mA
4-20 mA
+/-5 V
+/-10 C
RS485 /RS422
NMEA Signal
MODBUS
Ethernet
etc
Data is treated in just as many ways, as we:
Locate data
Collect data
Store data
Sort data
Analyze data
Use data onboard the Ship
Transmit and receive data between Ship and Shore
Use of data ashore

## Slide 5: When did we start to collect data onboard?
Weather data started in 1859
Naval vessels as frontrunners in 1930-85
Merchant vessels started collecting weather data after 1960
DATA, as we know it.
In use onboard merchant vessels: 1992-1995
Sending data to the office: 2000’ish
Maersk Fetcher – total of 16 alarm points for the engine room
Maersk Ras Laffan – Digital logbook (+10000 alarm points for the engine room).
Maersk releases 9 mio. weather observations from. 2012-2022
https://maritimedanmark.dk/?Id=47706 (Danish)

## Slide 6: Data sources onboard the vessel
All electrical manometers and gauges can be converted to data signals
Rudder movement
RPM
Pitch
Torque meter
Fuel Flow
Power, AUX, Shaft generator, Main switch board
Wind, force and directions, true/relative
Draughts
Movements due to wave action
Stress moments during loading/discharge, as well as underway
Trim
AIS
GPS
Boiler consumption, water, fuel, cemicals, temperature ect.
MAN-ES, ME engines, connected to shore

## Slide 7: Opsætning og brug.
Infrastructure
Demands:
  Standardized
  Open
  Generic
Auto logging
Demands:
  Standardized
  Ship-Owners data
Maintenance

## Slide 8
Searching for data collection points:
Find the relevant documentation for the equipment you will have to collect data from
Make a report and keep it simple
Use a step-by-step approach
i.e.
One color for each signal type
Light blue: +/- 10V signal
Green: 4-20mA signal
Purpol: Ethernet network
Yellow: VGA Cable

## Slide 9: What does the report provide?
Overview of the IT Structure onboard
Data needs to be sent ashore.
Therefore, you will need to get hold of the IT manager to get through.
Make sure to have all relevant material at your hand, for the smoothest communication
Protocol, IP-Addresses, Mac-addresses, Firewall, LAN port onboard the vessel to connect to and from.

## Slide 10: Data from Ship to Shore
Connectivity
Bandwith is limited
Satelite
3/4/5G
Starlink
http://www.satflare.com/track.asp?q=starlinkAll#TOP
WiFi

## Slide 11: The impact of data I:
Decision
support
Trim optimization
Speed optimization
Weather routing
Collision avoidance
Condition & performance monitoring
Turbo chargers
Propulsion
Hull performance
Etc.
Automated
reporting
Authorities
Voyage reporting
VTS
CII, EEDI, EEXI
Minimize emissions
FO - Savings
Minimize breakdowns
Remote diagnostics
Increase service intervals
Minimize the load on the crew

## Slide 12: The impact of data II:
Analysis
Hull performance
Route optimization
Performance optimization
Dynamic KPI’s
Awareness
Understanding impact and interaction of changing conditions
Comparing of sources validity Spoofing
Knowledge sharing
Comparison between ships
Driving continues improvements
Minimize emissions
FO Savings
Minimize breakdowns
FO Savings
FO Savings, for the rest of the fleet

## Slide 13: Smart Products
Ships
Offices
Owners
Charterers
Managers
Etc.

## Slide 14: Data Quality Inaccuracies Sources of Error

## Slide 15: Data quality
Is it crucial?
Who will use the data?
Correction of errors.
Work Arounds (good/bad).

## Slide 18: Data processing
The amount of data is critical!
Or is it?
It depends on:
Data quality
Frequency.
Is Realtime data needed?
What will you use the data for?
Is the crew better to collect data manually ?

## Slide 19: Use of the processed data
It is important that data is sorted due to the sheer amount of data
You will need good data, not peeks and down’s
Will data be valid and true, when sailing in bad weather?
What will we use the collected data for?
  Performance
  ML or AI ?
  ICS Systems
  AIS
  Whether data?
  Fuel figures
  Automated Reporting to authorities?

## Slide 20: Inaccuracies & Sources of Error
The old way
Noon reports
  High workload
  Human factor
New way
Auto logging
  High frequent sampling
  Low workload
  Automated sanity check

## Slide 22
How do we deal with faults in the data received?
Flow-meter
Torque meter

## Slide 23: 1 fault might start a chain reaction
Try to consider the following:
Which other systems onboard will use a specific signal/Data point?
How does each system use the data received ?
Are there a build in sanity check of the data received or will the system use the raw data ?

## Slide 24
Failiure on the Torque-meter
Torque-meter indicates an increased torque
ICS System
All tags using torque, for calculations will be wrong
What about the data they can see on the bridge ?
On some vessels one would like to sail at a constant load, this will be an issue here with afault on the torque meter
Data quality of the data that is send home ?
Performance systems are they effected ?
KPI Values for the vessel ?
Evaluating performance with sister vessels ?

## Slide 25: Action and ”Get out of Jail”
Be aware of the condition of all your sensors as well as the quality of data they collect.
Deck, Engine and Bridge!
What have changed since the sensor
worked properly?
  Service technichans?
  Callibrations ?
  Other faults
If your sensors are failing, then what ?
How will faulty data effect your vessels performance and KPI ?
Who is responsible ?

## Slide 26: On top of the sensor data Collection
Machine Learning
Breakdown of data
Fouling analyses
Route optimization
Trim advice onboard
Speed advice based on weather forecasts
and depth under keel
Propulsion optimization with
Q-Tagg
Frugal
Lean Marine
Installation of Flowmeters
Installation of Torque meters
Visualization for the crew

## Slide 27: MARPOL Annex VI Data collection ?
Regulation 22A
Collection and reporting of ship fuel oil consumption data 1 From calendar year 2019, each ship of 5,000 gross tonnage and above shall collect the data specified in appendix IX to this Annex, for that and each subsequent calendar year or portion thereof, as appropriate, according to the methodology included in the SEEMP
After existing appendix VIII, new appendices IX and X are inserted as follows:
Appendix IX
Information to be submitted to the IMO Ship Fuel Oil Consumption Database
Identity of the ship
IMO number
Period of calendar year for which the data is submitted
Start date (dd/mm/yyyy)
End date (dd/mm/yyyy)
Technical characteristics of the ship
Ship type, as defined in regulation 2 of this Annex or other (to be stated)
Gross tonnage (GT), Net tonnage (NT),Deadweight tonnage (DWT)
Power output (rated power) of main and auxiliary reciprocating internal combustion engines over 130 kW (to be stated in kW)
EEDI (if applicable)
Ice class
Fuel oil consumption, by fuel oil type in metric tonnes and methods used for collecting fuel oil consumption data
Distance travelled
Hours underway

## Slide 28: Smart Products
Ships
Offices
Owners
Charterers
Managers
Etc.